## Slide 1: Progress Update
2022-10-25
송희수

## Slide 2: ImageJ - ThunderSTORM
Raw data processing/feature enhancement & sub-diffraction localization of molecules (PSF fitting – weighted non-linear least-squares methods)
Create list of molecules with position, sigma (FWHM), and intensity
https://academic.oup.com/bioinformatics/article/30/16/2389/2748167
Wiki page: https://github.com/zitmen/thunderstorm/wiki

## Slide 3: ThunderSTORM – Image processing
Convolution with Wavelet filter

## Slide 4: ThunderSTORM - Parameters
이전 연구에도 ThunderSTORM을 사용한 것으로 확인됨.
이전에 쓰던 parameter history남아있음
Default parameter가 여러 연구에서 보편적으로 결과가 좋음
Default parameter와 이전 parameter 결과 비교

## Slide 5: Analysis Parameters (Raw Img+ Default)
Raw image를 넣고 analysis를 돌렸을 때의 spot detection 결과.
보기 좋게 하기 위해 analysis이후 별도로 간단한 contrast control & background subtraction 했음.
S1_W6_Px1_Py1_C3

## Slide 6: Analysis Parameters (Raw Img+ Previous)
낮은 localization 정확도
중복 detection
Default parameter에 pixel size만 도입해도 될 듯… (정확한 카메라 셋업이라는 가정하에)
Exosome localization에는 차이 없음. 단지 x, y (nm) position차이

## Slide 7: Analysis Parameters (Processed Img+ Default)
Normalization -> Background Subtraction -> ThunderSTORM analysis
거의 비슷하나, 약간의 localization 정확도 향상
Detect되지 않던 곳들(low intensity)도 detect -> 의미가 있는지는 확인필요

## Slide 8: Analysis Parameters (Processed Img+ Previous)
- 변화 있음. 그런데 긍정적인 변화인지는…

## Slide 9: Compare Channels (Same location)
C1
C2
C3
C4
S1_W6_Px1_Py1_C3

## Slide 10: C1
Noise? Or Spot?

## Slide 11: C2

## Slide 12: C3

## Slide 13: C4

## Slide 14: Example Result Table (C1)
Sigma = Std(Gaussian model used for fitting = weighted least squares)
Intensity = raw intensity. Total # of photons under fitted gaussian
Offset = Residuum after subtraction of fitted model
Bkgstd = Minimum intensity value
Chi2 = Error in raw intensities in a full fitting region
Uncertainty = Thompson formula (https://pubmed.ncbi.nlm.nih.gov/11964263/) –> Calculate std of x,y position
1 Spot

## Slide 15: Example Result Table (C3)
Further use normalized intensity values
The intensity in result table is no longer raw intensity if the processed image (contrast control & background subtraction) is used as input in ThunderSTORM (slide 7).

## Slide 16: Ideal Experimental Design
채널 별 (-) control images (Without fluorescence)
  Identify background signal
채널 별 fluorescence image
채널 No.5, (+) control image that fluoresce in all exosomes
  Provide ground truth of exosome position